## Slide 1: Hands-on Schedule
Abstractions
MLIR
Affine
SCF
MemRef
Arith
Linalg
Tensor
CMT
Firrtl
Stream
APS
hw
comb
seq
EDA Backends
Synthesis
Simulation
FPGA Deployment
Apps
Phys. Impl.
Circuit
GAA abstraction
Dyn pipeline
Synthesis
Architecture
Interconnect
Memory System
Task Scheduler
Compiler
C/C++ Frontend
Pattern-based
Retargeting
ML Pipeline
HDL Elaboration
ADL Language
Analysis
Transform
Scheduling
Flexible-levels
Instr. Finding
Part II: Synthesis
Presenter: Yitian Sun
Part III: Compiler
Presenter: Chenyun Yin
Part IV: Arch and Deployment
Presenter: Yuyang Zou
Part I: HDL and Instruction Finding
Presenter: Youwei Xiao

## Slide 2: Website
Project website: https://aps.ericlyun.me
Tutorial (today) page: https://aps.ericlyun.me/tutorials/aspdac-2026/
QR Code:

## Slide 3: Website
Project website: https://aps.ericlyun.me
Tutorial (today) page: https://aps.ericlyun.me/tutorials/aspdac-2026/
QR Code:
Download slides!

## Slide 4: Setup
Login our server
  First, you need a SSH key
  check if your SSH directory exists
    win: C:\Users\<username>/.ssh
    linux: $HOME/.ssh
    mac: /Users/<username>/.ssh
  if not exists, create one
    reference link
# Windows, open PowerShell
ssh-keygen -t ed25519 -C "<email>"
# Linux, open terminal
ssh-keygen -t ed25519 -C "<email>"
# Mac, open terminal
ssh-keygen -t ed25519 -C "<email>"
SSH public key can be found in <SSH>/id_ed25519.pub

## Slide 5: Setup
Login our server
  https://login.aps.ericlyun.me
  Enter your name and ssh key
  Follow the output to connect

## Slide 6: Setup
Login our server
  https://login.aps.ericlyun.me
  Enter your name and ssh key
  Follow the output to connect
Here is the SSH command for connection

## Slide 7: Setup
Login our server
  You can use PowerShell/terminal
  Or, you can use VSCode
    Ctrl-Shift-P / ⇧⌘P, type Remote: Show Remote Menu
      select SSH to install the extension
    Ctrl-Shift-P / ⇧⌘P, type Remote-SSH: Open SSH Configuration File
      paste
    Ctrl-Shift-P / ⇧⌘P, type Remote-SSH: Connect to Host
      pick “aps-tutorial”; pick “Linux”, “Yes”; wait for success
Here is the SSH configuration to be copied

## Slide 8: Setup
Login our server
  You can use PowerShell/terminal
  Or, you can use VSCode
    Where are the demos?
      Ctrl-J / ⌘J to open a terminal, run “ls /root”, you can see “aps” and “cmt2”
    Open the folder?
      Ctrl-K+O / ⌘K+O, select “/root/” and open
  Now we are ready to start the hands-on session!

## Slide 9: HDL and Instruction Finding
Speaker: Youwei Xiao
肖有为

## Slide 10: Part I: HDL and Instruction Finding
HDL
  What is Cement?
  Cmt2 basics and examples
  Circt-cmt2
Instruction finding
  ISAMORE (ASPLOS’26)
    finding reusable instructions via e-graph anti-unification

## Slide 11: Position of HDL in APS Flow
ISAMORE
APS
Frontend
APS
Synthesizer
FPGA
Flow
ASIC Flow
Cement CIRCT
Domain Applications
.cadl
RTL
Hardware
Software
Base Processors
Rocket
BOOM
CVA6
CV32E
APS
Compiler
Cross-level
ISAX Description
ISAX MLIR
Processor
RTL

## Slide 12: Cement: Better HDL and Framework for Chip Design
Traditional HDL
tedious hardware code
Embedded HDL (eHDL)
design hardware in advanced programming language (Scala, Python)
HLS: design hardware in C/C++
Cement (cmt1)
published at FPGA’24
Youwei Xiao, Zizhang Luo, Kexing Zhou, and Yun Liang. 2024. Cement: Streamlining FPGA Hardware Design with Cycle-Deterministic eHDL and Synthesis. FPGA '24. https://doi.org/10.1145/3626202.3637561
software-like control description
High-level HDL: describe hardware as rules
Cement (cmt2!)
keep evolving…
Rust-embedded HDL
rule-based design
?

## Slide 13: Today, we introduce cmt2!
software-like control description
Rust-embedded HDL
rule-based design
as the successor of …
Cement (cmt1)
published at FPGA’24
cmt2!

## Slide 14: Hello Rust World!
click [run] above fn main, or …
Cargo is Rust’s build system and package manager. It’s easy-to-use!
More user-friendly than sbt for Scala/Chisel!
create hello.rs file ↑
touch /root/cmt2/crates/cmtc/examples/hello.rs
cargo run --example hello
under directory /root/cmts

## Slide 15: Hello cmt2!
at the top of hello.rs
use clauses import cmt2’s eHDL and compiler features
itfc_declare! is a macro
macro in Rust transforms code at the token-level

## Slide 16: Hello cmt2!
macro is an advanced feature in Rust!
Please leave cmt2 developers to suffer😂
and… just use them!😁
The left code creates …
A module interface named A2B;
It has one input port a, one output port b, both of which have type T.
It exposes a method run for external world to invoke!
a:T
b:T
method run
A2B
at the top of hello.rs

## Slide 17: cmt2 is rule-based HDL
a:T
b:T
method run
Hardware logic is organized as rules – the execution unit!
Don’t be afriad!😁
Just consider one rule as a group of operations that execute together
In cmt2, we have two types of rules: method rules and always rules:
method rule need to be invoked (Bluespec method)
always rule runs actively (Bluespec rule)
A2B
at the top of hello.rs
rule-based design
cmt2!

## Slide 18: cmt2 is rule-based HDL
following itfc_declare!
fn starts a function!
The #[module] macro transfoms the function add1 to create a module of the interface A2B
a:T
b:T
method run
A2B
add1 of
UInt(4)
b=a+1
Now, types are given, rules are filled -- Module is completely described!

## Slide 19: cmt2 generates SystemVerilog
following fn add1
The new main function to call elaborate for the add1 module
click [run] above fn main, or …
cargo run --example hello
cat add1.sv

## Slide 20: Show features by examples
software-like control description
Rust-embedded HDL
rule-based design
as the successor of …
Cement (cmt1)
published at FPGA’24
cmt2!
FIR
GEMM

## Slide 21: Finite Impulse Response
./crates/cmtc/examples/fir.rs line 7-16
Rust-embedded HDL
cmt2!

## Slide 22: FIR Example1: fixed length
Parameters: type & coefficients
instantiate a
Reg as submodule
things to do after the method is invoked
reg %= xx is a syntax sugar for reg.write(xx)
./crates/cmtc/examples/fir.rs line 18-46
rule-based design

## Slide 23: FIR Example1: fixed length
shift the registers
implement the output method
./crates/cmtc/examples/fir.rs line 18-46

## Slide 24: FIR Example2: arbitrary length
An array of coefficients
Instantiate
a vector of
Regs
Input to the first reg
./crates/cmtc/examples/fir.rs line 48-78
Rust-embedded HDL

## Slide 25: FIR Example2: arbitrary length
Generate n-1 shifts with a software for expression
Make a multiply accumulate expression with functional programming
./crates/cmtc/examples/fir.rs line 48-78

## Slide 26: Explanation on the last expression
reg0
reg1
reg2
reg3
regs
a0
a1
a2
a3
a
iter()
zip()
For audiences that are not familiar with functional programming
map()
reduce()
Option<Sum>
Sum
unwrap()
Rust-embedded HDL

## Slide 27: FIR Example3: adder tree
generate an adder tree
a gen_fn generates hardware
./crates/cmtc/examples/fir.rs line 83-123

## Slide 28: FIR Example: Testbench preparation
the interface for the testbench
pass the DUT into the TB
tell the compiler this is a TB
instantiate DUT
./crates/cmtc/examples/fir.rs line 132-174

## Slide 29: FIR Example: Testbench inputs
make 10 inputs
make 10 always rules with different name
./crates/cmtc/examples/fir.rs line 132-174

## Slide 30: FIR Example: Testbench inputs
print during simulation
finish simulation at cycle 20
increase cycle counter
./crates/cmtc/examples/fir.rs line 132-174

## Slide 31: FIR Example: Elaboration & Simulation
cd /root/cmt2
cargo run –-example fir
cd ./tb/fir_tb1_ksim
make all
./FIR_s6
main function of Rust
Elaborate to generate simulation environment
Possible Outputs
./crates/cmtc/examples/fir.rs line 176-204

## Slide 32: GEMM
A Mem
B Mem
C Mem
MAC
F
S
M
memory as sub-interface
GEMM
write()
read()
simple methods to start computation and report finish
./crates/cmtc/examples/gemm.rs line 25-36
software-like control description
cmt2!

## Slide 33: GEMM Example: Software
GeMM in C using three for-loops
C
A
B
k
k
i
j

## Slide 34: GEMM Example: Preperation
calculate the address type
provide the memory instances to the interface
some register for loops
one MAC unit
one accumulator
./crates/cmtc/examples/gemm.rs line 38-97

## Slide 35: GEMM Example: FSM
keyword
a for loop
init: i=0
i<n i=0 => 0<n
update: i=i+1
i<n i=i+1 => i<n-1
i= 0 to n-1
j= 0 to n-1
./crates/cmtc/examples/gemm.rs line 38-97
software-like control description

## Slide 36: GEMM Example: FSM innermost body
for i in 0..n
  for j in 0..n
the following steps will be done in a sequence
generate n steps
feed memory address
get memory data
invoke MAC
accumulate result
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
Seq
step0
step1
step2
step3
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
amem.rd0
bmem.rd1
The same for all n steps
./crates/cmtc/examples/gemm.rs line 38-97

## Slide 37: GEMM Example: FSM last step
for i in 0..n
  for j in 0..n
Seq
step0
step1
step2
step3
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
amem.rd0
bmem.rd1
step n
amem.rd1
bmem.rd1
mac
acc
cmem.write
last mem read and MAC
write to cmem
./crates/cmtc/examples/gemm.rs line 38-97

## Slide 38: GEMM Example: Simulation
Expected results
Cycles= ( //k
//j
//i
= 4369
4370
+ 1 cycle to write finish
+ 1 cycle to init
+ 1 cycle to init
Commands to run simulation
cd /root/cmt2
cargo run –-example gemm
cd ./tb/gemm_ksim
make all
./GEMM_s16_i8

## Slide 39: GEMM unrolled Example: Interface Declare
Mem
Mem
C Mem
GEMM
Unrolled
MAC
MAC
MAC
MAC
Mem
Mem
Mem
Mem
Mem
Mem
FSM
Multi-bank 2D memory
./crates/cmtc/examples/gemm_unrolled.rs line 25-36

## Slide 40: GEMM unrolled Example
i
j
k
./crates/cmtc/examples/gemm_unrolled.rs
line 38-114

## Slide 41: GEMM unrolled Example: innermost
Each inner loop have n/factor+1 steps
for i in 0..n
  for j in 0..n
read factor memory banks at the same time
invoke factor MACs and accumulate
get the sum of all accumulators
write to c memory
./crates/cmtc/examples/gemm_unrolled.rs
line 38-114

## Slide 42: GEMM unrolled Example: Simulation
1298
Commands to run simulation
Factor=4 results
Cycles= ( //k
//j
//i
= 1297
4370/12983.37
cd /root/cmt2
cargo run –-example gemm_unrolled
cd ./tb/gemm_unrolled_ksim
make all
./GEMMUnrolled_s16_i8

## Slide 43: We’ve integrated Cement into APS!
Traditional HDL
tedious hardware code
Embedded HDL (eHDL)
design hardware in advanced programming language (Scala, Python)
HLS: design hardware in C/C++
Cement (cmt1)
published at FPGA’24
Youwei Xiao, Zizhang Luo, Kexing Zhou, and Yun Liang. 2024. Cement: Streamlining FPGA Hardware Design with Cycle-Deterministic eHDL and Synthesis. FPGA '24. https://doi.org/10.1145/3626202.3637561
software-like control description
High-level HDL: describe hardware as transactions/rules
Cement (cmt2!)
Keep evolving…
Rust-embedded HDL
rule-based design
①
②
circt-cmt2
③
Migration for APS integration

## Slide 44: circt-cmt2
We implement cmt2 as a new dialect in CIRCT
MLIR/CIRCT Dialects
Affine
SCF
MemRef
Arith
Linalg
Tensor
Stream
APS
Cmt2
FIRRTL
HW
Comb
…
APS synthesis flow
Cmt2ToFIRRTL conversion
code (or cat) circt/test/Dialect/Cmt2/hello.mlir

## Slide 45: circt-cmt2 EDSL
For productive programming circt-cmt2, we provide a C++-based EDSL. It is used by APS’s synthesizer.
code circt/examples/ECMT2/hello_v3.cpp
construct

## Slide 46: Instruction Finding
ISAMORE
APS
Frontend
APS
Synthesizer
FPGA
Flow
ASIC Flow
Cement CIRCT
Domain Applications
.cadl
RTL
Hardware
Software
Base Processors
Rocket
BOOM
CVA6
CV32E
APS
Compiler
Cross-level
ISAX Description
ISAX MLIR
Processor
RTL

## Slide 47: Reusability is a key concern
We should find reusable instructions to customize.
Domain Applications
If we have …
and many other expressions in applications.
A. Multiple custom instructions
Three custom instructions.
Costly, redundant
B. Syntactic merging: prior work
Ad-hoc
HW-inefficient
C. Semantically reusable instruction
(ideal)
General, efficient

## Slide 48: Find Reusable Instructions via E-Graph Anti-Unification
E-graph is a data structure to compactly represent equivalent terms.
Initial E-graph
E-node: term or subexpression
E-class: contains equivalent e-nodes
Saturated (partially) E-graph

## Slide 49: Find Reusable Instructions via E-Graph Anti-Unification
Anti-unification is the process of constructing a generalization common to two given symbolic expressions
finds common pattern
① Green terms are found common
② Red terms are found common
①
②
Anti-unify

## Slide 50: ISAMORE Framework
We’ll present ISAMORE at ASPLOS 2026!
ISAMORE
Domain Applications
.cadl
We are working on ISAMORE’s integration into APS.

## Slide 51: Hardware Synthesis
Speaker: Yitian Sun
孙逸天

## Slide 52: Before Getting Started
Please run pixi shell in the ~/aps directory
CHECK：
pixi shell
(aps-mlir) root@server:~/aps

## Slide 53: Outline
Challenges in ASIP hardware synthesis
APS hardware synthesis flow
  Cross-level architectural language (CADL)
  MLIR & APS dialect
  Parsing CADL into MLIR
  Optimization and synthesis transformations

## Slide 54: Challenges in ASIP Hardware Synthesis
Open-source
Agile
Optimized
RTL
SCAIE-V (DAC ’22)
Longnail (ASPLOS ’24)
...
ASIP Designer, Codasip, ...
APS
Academic works
Verilog
Chisel (Chipyard)
...
Commercial tools
Different ISAX customization methods

## Slide 55: Hardware Synthesis Flow
CADL
Pre-Opt
MLIR
Scheduled
MLIR
Verilog
Parsing
Optimization
Scheduling
Hardware
Generation
Hardware MLIR Representation
Elaboration
Untimed representation
Timed representation
Software-like semantics:
Affine dialect
SCF dialect
Arith dialect
APS dialect
...
Hardware semantics:
FIRRTL dialect
CMT2 dialect
...
High-level description of ISAX

## Slide 56: Hardware Synthesis Flow
CADL
Pre-Opt
MLIR
Scheduled
MLIR
Verilog
Parsing
Optimization
Scheduling
Hardware
Generation
Hardware MLIR Representation
Elaboration
Untimed representation
Timed representation
Software-like semantics:
Affine dialect
SCF dialect
Arith dialect
APS dialect
...
Hardware semantics:
FIRRTL dialect
CMT2 dialect
...
High-level description of ISAX

## Slide 57: Abstraction of Processor-ISAX Interface
EX
...
...
Custom FUs
Custom
Coprocessors
Req.
Resp.
Dedicated
Accelerators
Chip
CPU Core
Different Processors
Pipeline stages
Memory interface
...
Different ISAX implementation approaches
Custom function units
Custom coprocessors
Dedicated accelerators
Different ISAX interfaces
RoCC
CV-X-IF
...
A unified abstraction of processor-ISAX interface is needed!

## Slide 58: APS-Itfc
A transactional abstraction of processor-ISAX interface
Transaction | Semantics
Issue Req | Receive a new ISAX from the core
GPR Req | Receive source operands
Rd/WrMem Req | Request a single memory access
Rd/WrMem Resp | Receive a single memory access
Rd/WrBlkMem Req | Request a block memory access
Rd/WrBlkMem Resp | Receive a block memory access
Result Resp | Send the final result to the core

## Slide 59: CADL
CADL is designed to simplify the specification of optimized ISAXs
CADL describes
  ISAX encoding
  Untimed behavior of ISAXs
    APS-iftc
    Scratchpad memory
    Arithmetic
    Control flow
    Optimization directives
#[opcode(7'b0101011)]
#[funct7(7'b0000000)]
rtype hello(
rs1: u5,
rs2: u5,
rd: u5
) {
let a: u32 = _irf[rs1];
let b: u32 = _irf[rs2];
let c: u32 = a + b;
_irf[rd] = c;
}

## Slide 60: Hello CADL
#[opcode(7'b0101011)]
#[funct7(7'b0000000)]
rtype hello(
rs1: u5,
rs2: u5,
rd: u5
) {
let a: u32 = _irf[rs1];
let b: u32 = _irf[rs2];
let c: u32 = a + b;
_irf[rd] = c;
}
ISAX encoding
Operands of
the ISAX
Read source
operands
Write back
GPR Req transaction
Result Resp transaction
# Run the synthesis flow
# Results in $APS/tutorial/outputs/hello
./tutorial/s1-hello-synth.sh
$APS/tutorial/cadl/hello.cadl

## Slide 61: GEMV Example: Software
GeMV in C using two for-loops
for (int i = 0; i < 4; i++) {
int acc = 0;
for (int j = 0; j < 4; j++) {
acc += a[i][j] * b[j];
}
c[i] = acc;
}
A
B
i
j
C
i
j

## Slide 62: GEMV Example: Scratchpad Memory
#[partition_dim_array([0])]
#[partition_factor_array([4])]
#[partition_cyclic_array([1])]
static matrix: [i32; 16];
#[partition_dim_array([0])]
#[partition_factor_array([4])]
#[partition_cyclic_array([1])]
static vec: [i32; 4];
static result: [i32; 4];
static acc: i32;
Array partitioning directives
0
1
2
3
matrix
12
13
14
15
...
Array partitioning
matrix_0
matrix_1
0
4
8
12
1
5
9
13
2
6
10
14
3
7
11
15
matrix_2
matrix_3
Allocate scratchpad memory
to store arrays or elements
$APS/tutorial/cadl/vgemv3d.cadl
4 banks:
Each bank is an independent memory unit with its own ports

## Slide 63: GEMV Example: Block-Wise Memory Access
#[opcode(7'b1111011)]
#[funct7(7'b0110001)]
rtype gemv(rs1: u5, rs2: u5, rd: u5) {
// omitted ...
matrix[0+:]=_burst_read[in_addr+:16];
vec[0] = _mem[in_addr + 64];
vec[1] = _mem[in_addr + 68];
vec[2] = _mem[in_addr + 72];
vec[3] = _mem[in_addr + 76];
// to be introduced ...
}
Block-wise memory read
RdBlkMem Req & Resp transactions
Load 16 elements from the memory to the SPM “matrix”
Load 4 elements from the memory to the SPM “vec”
$APS/tutorial/cadl/vgemv3d.cadl
Element-wise memory read
RdMem Req & Resp transactions

## Slide 64: GEMV Example: Control Flow
rtype gemv(rs1: u5, rs2: u5, rd: u5) {
// omitted ...
with i: u32 = (0, i_) do {
acc = 0;
[[unroll(4)]]
with j: u32 = (0, j_) do {
acc = acc + matrix[i*4+j] * vec[j];
let j_: u32 = j + 1;
} while (j_ < 4);
result[i] = acc;
let i_: u32 = i + 1;
} while (i_ < 4);
// to be introduced ...
}
Nested loops
Calculate the GEMV
Loop unrolling directive
Unroll the inner loop
$APS/tutorial/cadl/vgemv3d.cadl

## Slide 65: GEMV Example: Element-Wise Memory Access
rtype gemv(rs1: u5, rs2: u5, rd: u5) {
// omitted ...
_mem[out_addr] = result[0];
_mem[out_addr + 4] = result[1];
_mem[out_addr + 8] = result[2];
_mem[out_addr + 12] = result[3];
irf_rd[rd] = 0;
}
Write back
Element-wise memory write
WrMem Req & Resp transaction
Store the results from the the SPM “results” to the memory
Result Resp transaction
$APS/tutorial/cadl/vgemv3d.cadl

## Slide 66: Hardware Synthesis Flow
CADL
Pre-Opt
MLIR
Scheduled
MLIR
Verilog
Parsing
Optimization
Scheduling
Hardware
Generation
Hardware MLIR Representation
Elaboration
Untimed representation
Timed representation
Software-like semantics:
Affine dialect
SCF dialect
Arith dialect
APS dialect
...
Hardware semantics:
FIRRTL dialect
CMT2 dialect
...
High-level description of ISAX

## Slide 67: MLIR
A novel compiler infrastructure that greatly facilitates the implementation of user-defined IRs and transformations
  Reuse IRs and extend new IRs
%res:1 = "mydialect.morph"(%arg0) { some_attr = true }
: (!mydialect<“custom_type”>) -> (i32)
Name of the results
Number of value returned
Dialect prefix
Op ID
Argument
Attribute
Dialect-specific type
Type
Triton
CIRCT
Widely used in recent compilers
Generic representation of MLIR operations

## Slide 68: APS Dialect
APS dialect is the MLIR version of APS-itfc
GPR Req
_irf[rs1]
APS-Itfc
CADL
APS Dialect
aps.readrf
Result Resp
_irf[rd]
aps.writerf
WrMem
_mem[x]
aps.memstore
RdBlkMem
_burst_read[x +: s]
aps.memburstload
RdMem
_mem[x]
aps.memload
$APS/tutorial/outputs/hello/0_hello_preopt.mlir
module {
func.func @flow_hello(
%arg0: i5,
%arg1: i5,
%arg2: i5
) {
%0 = aps.readrf %arg0 : i5 -> i32
%1 = aps.readrf %arg1 : i5 -> i32
%2 = arith.addi %0, %1 : i32
aps.writerf %arg2, %2 : i5, i32
return
}
}

## Slide 69: GEMV Example: Parsing CADL to MLIR
#[partition_dim_array([0])]
#[partition_factor_array([4])]
#[partition_cyclic_array([1])]
static matrix: [i32; 16];
#[partition_dim_array([0])]
#[partition_factor_array([4])]
#[partition_cyclic_array([1])]
static vec: [i32; 4];
static result: [i32; 4];
static acc: i32;
module {
memref.global @_cpu_memory
memref.global @matrix {
partition info ...
}
memref.global @vec {
partition info ...
}
memref.global @result
memref.global @acc
func.func ...
}
CADL
MLIR
CPU memory
Scratchpad mem
$APS/tutorial/outputs/vgemv3d/
0_vgemv3d_preopt.mlir (lines 1-6)
Use the memref dialect to express memory

## Slide 70: GEMV Example: Parsing CADL to MLIR
%0 = aps.readrf %arg0
%1 = aps.readrf %arg1
%2 = memref.get_global @matrix
%c0_i32 = arith.constant 0
%c16_i32 = arith.constant 16
aps.memburstload %0, (%2) [%c0_i32], %c16_i32
#[opcode(7'b1111011)]
#[funct7(7'b0110001)]
rtype gemv(rs1: u5, rs2: u5, rd: u5) {
let in_addr: u32 = _irf[rs1];
let out_addr: u32 = _irf[rs2];
matrix[0+:]=_burst_read[in_addr+:16];
// to be introduced ...
}
CADL
MLIR
APS-itfc is lower to the APS dialect!
Read operands
Block-wise
memory access
$APS/tutorial/outputs/vgemv3d/
0_vgemv3d_preopt.mlir (lines 8-13)

## Slide 71: GEMV Example: Parsing CADL to MLIR
rtype gemv(rs1: u5, rs2: u5, rd: u5) {
// omitted ...
with i: u32 = (0, i_) do {
acc = 0;
[[unroll(4)]]
with j: u32 = (0, j_) do {
acc = acc + matrix[i*4+j] * vec[j];
let j_: u32 = j + 1;
} while (j_ < 4);
result[i] = acc;
let i_: u32 = i + 1;
} while (i_ < 4);
// to be introduced ...
}
scf.for %arg3 = %c0_i32 to %c4_i32 step %c1_i32 {
aps.globalstore %c0_i32, @acc
scf.for %arg4 = %c0_i32 to %c4_i32 step %c1_i32 {
%23 = aps.globalload @acc
%24 = arith.muli %arg3, %c4_i32
%25 = arith.addi %24, %arg4
%26 = aps.memload %2[%25]
%27 = aps.memload %4[%arg4]
%28 = arith.muli %26, %27
%29 = arith.addi %23, %28
aps.globalstore %29, @acc
} {unroll = 4 : i32}
%21 = aps.globalload @acc
%22 = memref.get_global @result
aps.memstore %21, %22[%arg3]
}
CADL
MLIR
Use the SCF dialect to express loops
Use the MLIR attributes to represent directives
Loop unrolling
$APS/tutorial/outputs/vgemv3d/
0_vgemv3d_preopt.mlir (lines 36-51)

## Slide 72: GEMV Example: Parsing CADL to MLIR
rtype gemv(rs1: u5, rs2: u5, rd: u5) {
// omitted ...
_mem[out_addr] = result[0];
_mem[out_addr + 4] = result[1];
_mem[out_addr + 8] = result[2];
_mem[out_addr + 12] = result[3];
irf_rd[rd] = 0;
}
%14 = aps.memload %13[%c0_i32]
aps.memstore %14, %3[%1]
%15 = aps.memload %13[%c1_i32]
%16 = arith.addi %1, %c4_i32
aps.memstore %15, %3[%16]
%c2_i32 = arith.constant 2
%17 = aps.memload %13[%c2_i32]
%c8_i32 = arith.constant 8
%18 = arith.addi %1, %c8_i32
aps.memstore %17, %3[%18]
%c3_i32 = arith.constant 3
%19 = aps.memload %13[%c3_i32]
%c12_i32 = arith.constant 12
%20 = arith.addi %1, %c12_i32
aps.memstore %19, %3[%20]
aps.writerf %arg2, %c0_i32
Write back
Element-wise
memory write
CADL
MLIR
APS-itfc is lower to the APS dialect!
$APS/tutorial/outputs/vgemv3d/
0_vgemv3d_preopt.mlir (lines 53-66)

## Slide 73: Hardware Synthesis Flow
CADL
Pre-Opt
MLIR
Scheduled
MLIR
Verilog
Parsing
Optimization
Scheduling
Hardware
Generation
Hardware MLIR Representation
Elaboration
Untimed representation
Timed representation
Software-like semantics:
Affine dialect
SCF dialect
Arith dialect
APS dialect
...
Hardware semantics:
FIRRTL dialect
CMT2 dialect
...
High-level description of ISAX

## Slide 74: High-Level Synthesis
High-level synthesis (HLS) allows the designers to design hardware at a high-level abstraction

## Slide 75: Optimization Passes: Memory Map
module {
aps.memorymap {
aps.mem_entry "acc" : banks([@acc]), base(0), size(4), count(1), cyclic(0)
aps.mem_entry "matrix" : banks([@matrix]), base(4), size(64), count(1), cyclic(1)
aps.mem_entry "result" : banks([@result]), base(128), size(16), count(1), cyclic(0)
aps.mem_entry "vec" : banks([@vec]), base(144), size(16), count(1), cyclic(1)
aps.mem_finish
}
memref.global @_cpu_memory : memref<1024xi32>
// omitted ...
}
Memory map
Maintain a mapping from memory names to memory metadata (e.g., partitions and addresses)
Generated by the memory-map pass
$APS/tutorial/outputs/vgemv3d/
1_vgemv3d_memory-map.mlir (lines 2-8)

## Slide 76: Optimization Passes: Raising to Affine
scf.for %arg3 = %c0_i32 to %c4_i32 step %c1_i32 {
aps.globalstore %c0_i32, @acc
scf.for %arg4 = %c0_i32 to %c4_i32 step %c1_i32 {
%23 = aps.globalload @acc
%24 = arith.muli %arg3, %c4_i32
%25 = arith.addi %24, %arg4
%26 = aps.memload %2[%25]
%27 = aps.memload %4[%arg4]
%28 = arith.muli %26, %27
%29 = arith.addi %23, %28
aps.globalstore %29, @acc
} {unroll = 4 : i32}
%21 = aps.globalload @acc
%22 = memref.get_global @result
aps.memstore %21, %22[%arg3]
}
affine.for %arg3 = 0 to 4 {
aps.globalstore %c0_i32, @acc : i32
affine.for %arg4 = 0 to 4 {
%31 = aps.globalload @acc : i32
%32 = affine.load %2[%arg4 + %arg3 * 4] : memref<16xi32>
%33 = affine.load %7[%arg4] : memref<4xi32>
%34 = arith.muli %32, %33 : i32
%35 = arith.addi %31, %34 : i32
aps.globalstore %35, @acc : i32
} {unroll = 4 : i32}
%29 = aps.globalload @acc : i32
%30 = memref.get_global @result : memref<4xi32>
affine.store %29, %30[%arg3] : memref<4xi32>
}
Before the raising passes
After the raising passes
Affine dialect simplifies the analysis in loop unrolling and array partitioning passes
Affine memory access must be expressed as affine expressions
$APS/tutorial/outputs/vgemv3d/
2_vgemv3d_affine.mlir (lines 46-59)

## Slide 77: Optimization Passes: Loop Unrolling
affine.for %arg3 = 0 to 4 {
aps.globalstore %c0_i32, @acc : i32
affine.for %arg4 = 0 to 4 {
%31 = aps.globalload @acc : i32
%32 = affine.load %2[%arg4+%arg3*4]
%33 = affine.load %7[%arg4]
%34 = arith.muli %32, %33 : i32
%35 = arith.addi %31, %34 : i32
aps.globalstore %35, @acc : i32
} {unroll = 4 : i32}
%29 = aps.globalload @acc : i32
%30 = memref.get_global @result
affine.store %29, %30[%arg3]
}
affine.for %arg3 = 0 to 4 {
aps.globalstore %c0_i32, @acc : i32
%29 = aps.globalload @acc : i32
%30 = affine.load %2[%c0 + %arg3 * 4]
%31 = affine.load %7[%c0]
%32 = arith.muli %30, %31 : i32
%33 = arith.addi %29, %32 : i32
aps.globalstore %33, @acc : i32
%34 = affine.apply #map(%c0)
%35 = aps.globalload @acc : i32
%36 = affine.load %2[%34 + %arg3 * 4]
%37 = affine.load %7[%34]
%38 = arith.muli %36, %37 : i32
%39 = arith.addi %35, %38 : i32
aps.globalstore %39, @acc : i32
// repeat for 4 times
}
Before the hls-unroll pass
After the hls-unroll pass
Loop unrolling aims to expose more parallelism
$APS/tutorial/outputs/vgemv3d/
3_vgemv3d_unroll.mlir (lines 50-82)

## Slide 78: Optimization Passes: Array Partitioning
affine.for %arg3 = 0 to 4 {
aps.globalstore %c0_i32, @acc : i32
%29 = aps.globalload @acc : i32
%30 = affine.load %2[%c0 + %arg3 * 4]
%31 = affine.load %7[%c0]
%32 = arith.muli %30, %31 : i32
%33 = arith.addi %29, %32 : i32
aps.globalstore %33, @acc : i32
%34 = affine.apply #map(%c0)
%35 = aps.globalload @acc : i32
%36 = affine.load %2[%34 + %arg3 * 4]
%37 = affine.load %7[%34]
%38 = arith.muli %36, %37 : i32
%39 = arith.addi %35, %38 : i32
aps.globalstore %39, @acc : i32
// repeat for 4 times
}
affine.for %arg3 = 0 to 4 {
%35 = affine.load %2[%arg3] : memref<4xi32>
%36 = affine.load %10[0] : memref<1xi32>
%37 = arith.muli %35, %36 : i32
%38 = affine.load %3[%arg3] : memref<4xi32>
%39 = affine.load %11[0] : memref<1xi32>
%40 = arith.muli %38, %39 : i32
%41 = arith.addi %37, %40 : i32
%42 = affine.load %4[%arg3] : memref<4xi32>
%43 = affine.load %12[0] : memref<1xi32>
%44 = arith.muli %42, %43 : i32
%45 = arith.addi %41, %44 : i32
%46 = affine.load %5[%arg3] : memref<4xi32>
%47 = affine.load %13[0] : memref<1xi32>
%48 = arith.muli %46, %47 : i32
%49 = arith.addi %45, %48 : i32
aps.globalstore %49, @acc : i32
%50 = memref.get_global @result : memref<4xi32>
affine.store %49, %50[%arg3] : memref<4xi32>
}
Before the array-partition pass
After the array-partition pass
Access the same memory
Access different memories
Array partitioning aims to eliminate dependencies
$APS/tutorial/outputs/vgemv3d/
4_vgemv3d_array-partition.mlir (lines 58-77)

## Slide 79: HLS Scheduling
module {
tor.design @aps_isaxes {
tor.func @hello(%arg0: i5, %arg1: i5, %arg2: i5) {
tor.timegraph (0 to 2) {
tor.succ 1 : [0 : i32] [{type = "static:1"}]
tor.succ 2 : [1 : i32] [{type = "static:1"}]
}
%0 = aps.readrf %arg0 {st = 0, end = 1}
%1 = aps.readrf %arg1 {st = 0, end = 1}
%2 = tor.addi %0 %1 {st = 1, end = 2}
aps.writerf %arg2, %2 {st = 1, end = 2}
tor.return
}
} {schedule = true}
}
SDC constraints
Data dependency constraints
Resource constraints
...
0
1
2
3
aps.readrf
aps.readrf
tor.addi
aps.writerf
1
1
0
Longest path
TOR dialect: provided by MLIR-based HLS tool Hector
$APS/tutorial/outputs/hello/
1_hello_scheduled.mlir
System of difference constraints formulation

## Slide 80: HLS Scheduling
From SDC result to pipeline stages
aps.readrf: cycle 0~1
aps.readrf: cycle 0~1
aps.memburstload: cycle 1~16
...
Time graph
tor.timegraph (0 to 21){
tor.succ 1 : [0 : i32] [{type = "static:1"}]
...
tor.succ 6 : [5 : i32] [{type = "static"}]
tor.succ 7 : [6 : i32] [{type = "static:1"}]
tor.succ 8 : [7 : i32] [{type = "static:1"}]
tor.succ 9 : [8 : i32] [{type = "static:1"}]
...
tor.succ 14 : [13 : i32] [{type = "static:1"}]
}
Each edge in time graph is a pipeline stage
SDC Result
$APS/tutorial/outputs/vgemv3d/
5_vgemv3d_scheduled.mlir (lines 26-51)

## Slide 81: Hardware Synthesis Flow
CADL
Pre-Opt
MLIR
Scheduled
MLIR
Verilog
Parsing
Optimization
Scheduling
Hardware
Generation
Hardware MLIR Representation
Elaboration
Untimed representation
Timed representation
Software-like semantics:
Affine dialect
SCF dialect
Arith dialect
APS dialect
...
Hardware semantics:
FIRRTL dialect
CMT2 dialect
...
High-level description of ISAX

## Slide 82: Lower to cmt2
// ...
cmt2.rule @inst7b31_loop_1_loop_block_0_slot_10_rule {
%c1_ui1 = firrtl.constant 1 : !firrtl.uint<1>
cmt2.return %c1_ui1 : !firrtl.uint<1>
} {
%0 = cmt2.call @inst7b31_loop_1_loop_block_0_token_fifo_s9 @deq()
%1 = cmt2.call @scratchpad_pool @matrix_0_read_1()
%2 = cmt2.call @inst7b31_loop_1_loop_block_0_fifo_s9_s10_v0 @deq()
%3 = firrtl.mul %1, %2
%4 = firrtl.bits %3 31 to 0
// ...
$APS/tutorial/outputs/vgemv3d/
6_vgemv3d_cmt2.mlir (lines 2140-2148)
Time graph
Each pipeline stage corresponds to a transaction

## Slide 83: Compiler
Speaker: Chenyun Yin
殷晨云

## Slide 84: Outline
Motivation
  Manual Intrinsic Insertion
  Pattern Matching
Background: E-graph
  Introduction to E-graph
  e-graph + MLIR
Key Techniques
  E-graph Construction
  Semantic Translation
  Hybrid Rewrite
  Skeleton-components Matching

## Slide 85: Quick Start
Run
  cd ~/aps/ && pixi run tutorial-compiler-demo
Get
Port forwarding
click
Open web browser, access:
http://localhost:8501

## Slide 86: APS Design Flow
ISAMORE
APS
Frontend
APS
Synthesizer
FPGA
Flow
ASIC Flow
Cement CIRCT
Domain Applications
.cadl
RTL
Hardware
Base Processors
Rocket
BOOM
CVA6
CV32E
APS
Compiler
Cross-level
ISAX Description
ISAX MLIR
Processor
RTL
Software

## Slide 87: APS-Compiler’s Task
APS compiler takes application C code and ISAXs’ CADL as inputs, to generate a binary utilizing given ISAXs.
Matching
#[opcode(7'b0101011)]
#[funct7(7'b0110001)]
rtype vgemv3d_vv(rs1:u5,rs2:u5,rd:u5){
let addr: u32 = _irf[rs1];
let out_addr: u32 = _irf[rs2];
matrix[0+:] = _burst_read[addr+: 16];
...
_irf[rd] = 0;
}
ISAX CADL
800001a8 <gemv>:
800001a8: 62b5752b .insn 4, 0x62b5752b
800001ac: 00000513 li a0,0
800001b0: 00008067 ret
Retargetable Compiling
Newly added ISAXs
App C code
#include <stdint.h>
#include <stdio.h>
uint8_t gemv(int32_t *array1, int32_t *array2) {
...
}
int main(void) {
gemv(input_data, output_data);
softmax(...);
...
}

## Slide 88: Manual Intrinsic Insertion
In conventional ways, programmers call ISAX by using intrinsic explicitly in the source code
asm volatile (".insn r 0x0B, 0, 0x3, %0, %1, %2” : "=r"(rd) : "r"(rs1), "r"(rs2))
Apps
ISAXs
Code Variants
Enormous
Design Space
Transformer
CNN
GNN
GEMV
GEMM
DECOMP
Kernel Fusion
Algebra
Transformation
Scheduling
Manual intrinsic insertion does not scale!

## Slide 89: Automatic Pattern Matching
for i=0 to 4:
for j=0 to 4:
acc+=a[i<<2+j]*b
yield acc
store acc
ISAX
Control Flow
Computation Pattern
Side-effects
Complex
structures!
a[i<<2+j]*b
Loop unroll
Loop split
Loop reorder
a[j+i<<2]*b
a[i*4+j]*b
Too much
variants!
…
Traditional
Pattern Matcher
Syntactic matching
Brittle under control-flow variations
Hard to match
…

## Slide 90: Our Solution
for i=0 to 4:
for j=0 to 4:
acc+=...
yield acc
Skeleton-components match
2
m
1
--affine-loop-unroll
+
Loop
Passes
E-graph+
Hybrid
rewriting
Complex
structures!
Too much
variants!
Challenges
APS Compiler’s Solutions
for i=0 to 4:
for j=0 to 4:
acc+=a[i<<2+j]*b
yield acc
store acc
<<
x

## Slide 91: Introduction to E-graphs: Definitions
e-graph: A data structure that compactly represents a large set of equivalent expressions
  e-node: A functional operator or a constant (e.g.,+,*,5).
  e-class: A set of e-nodes that are mathematically or logically equivalent
e-class
e-node
<<
2
m
1
x
e-node’s children are e-classes!
m x 2 ‘s
semantic space

## Slide 92: Introduction to E-graphs: Operations
Rewrite = e-matching + union (non-destructive)
  e-matching: searching a pattern
  union: merge two e-nodes into a single e-class
Extract: select the optimal candidate
Rewrite
Extract
<<
2
m
1
x
2
m
x
rule : 2 x ?a?a << 1
2
m
x
e-matching: 2 x ?a
union: ?a << 1
<<
2
m
1
x
<<
m
1
extractor
x: 100
<<: 2
cost model

## Slide 93: Introduction to E-graphs: Tools
egglog:
  PLDI’23
  Better Together: Unifying Datalog and Equality Saturation
Type definition
Expr declaration
Rewrite rules
Extraction
DSL
(datatype Expr
(Num i64)
(Var String)
(Add Expr Expr)
(Mul Expr Expr))
(let expr1 (Mul (Num 2) (Mul (Var "x") (Num 3)))
(rewrite (Add x y) (Add y x))
(rewrite (Mul x y) (Mul y x))
(rewrite (Mul x (Mul y z)) (Mul (Mul x y) z))
(extract expr1)

## Slide 94: Egglog Demo
Click here
Click here
Exprs after extraction
E-Graphs
Click here

## Slide 95: Egglog Demo
(a * 2) / 2
Rewrite: a * 2  a << 1
Rewrite: (a * b) / c  a * (b / c)
Rewrite: a / a  1
Rewrite: a * 1  a
Good for dataflow transformation!

## Slide 96: Control Flow Transformations
MLIR control flow pass
  transform the program’s control-flow graph (basic blocks, branches, and loops) for optimization
loop
unroll
loop
fusion

## Slide 97: Combining e-graph and MLIR
E-Graph: the core data structure
Utilizing MLIR passes as external rewrites to non-destructively explore the control-flow semantic-equivalence space
for
store
x
<<
i
4
2
1
step
omit loop bounds
for (0, 4, 1):
A[i] = i * 4;
omit load…
for (0, 4, 2):
A[i] = i * 4;
A[i+1] = (i+1) * 4;
loop unroll 2
extract
for
store
store
step
union
…

## Slide 98: APS Compiler Workflow
Custom Instr(CADL)
Hybrid Rewrite Engine
Skeleton-components matching
Semantic Translation
Binary
Lowering passes
Existing tools
Key techniques
Initial
e-graph
Application (c-code)
Polygeist
Application
MLIR
E-graph
Construction
dataflow
rewrite rules
MLIR
passes
ISAX
MLIR

## Slide 99: Semantic Translation
Custom Instr(CADL)
Hybrid Rewrite Engine
Skeleton-components matching
Semantic Translation
Binary
Lowering passes
Existing tools
Key techniques
Initial
e-graph
Application (c-code)
Polygeist
Application
MLIR
E-graph
Construction
dataflow
rewrite rules
MLIR
passes
ISAX
MLIR

## Slide 100: Semantic Translation
module {
func.func @vgemv3d_vv(%arg0: memref<?xi32>, %arg1: memref<?xi32>) -> i8 {
...
scf.for %arg2 = %c0 to %c2 step %c1 {
%3 = scf.for %arg3 = %c0 to %c4 step %c1 iter_args(%arg4 = %c0_i32) -> (i32) {
...
scf.yield %18 : i32
}
memref.store %3, %arg1[%4] : memref<?xi32>
}
return %c0_i8 : i8
}
}
Translating CADL into high-level MLIR computation patterns for matching
Just high-level patterns
#[opcode(7'b0101011)]
#[funct7(7'b0110001)]
rtype vgemv3d_vv(rs1: u5, rs2: u5, rd: u5) {
let addr: u32 = _irf[rs1];
let out_addr: u32 = _irf[rs2];
matrix[0 +: ] = _burst_read[addr +: 16];
with i: u32 = (0, i_) do {
[[unroll(4)]]
with j: u32 = (0, j_) do {
…
} while (j_ < 4);
} while (i_ < 4);
_irf[rd] = 0;
}
Hardware information

## Slide 101: Hands-on Translation
Click
cadl
source
Translated
MLIR

## Slide 102: APS Compiler Workflow
Custom Instr(CADL)
Hybrid Rewrite Engine
Skeleton-components matching
Semantic Translation
Binary
Lowering passes
Existing tools
Key techniques
Initial
e-graph
Application (c-code)
Polygeist
Application
MLIR
E-graph
Construction
dataflow
Rewrite rules
MLIR
passes
ISAX
MLIR

## Slide 103: E-graph Construction
%7 = scf.for %arg3 = %c0 to %c4 step %c1 iter_args(%arg4 = %c0_i32) -> (i32) {
%10 = arith.index_cast %arg3 : index to i32
%11 = arith.addi %6, %10 : i32
%12 = arith.index_cast %11 : i32 to index
%13 = memref.load %arg0[%12] : memref<?xi32>
%14 = arith.addi %10, %c16_i32 : i32
%15 = arith.index_cast %14 : i32 to index
%16 = memref.load %arg0[%15] : memref<?xi32>
%17 = arith.muli %13, %16 : i32
%18 = arith.addi %arg4, %17 : i32
scf.yield %18 : i32
}
Control flow in MLIR
control flow ops
regions
terminators

## Slide 104: E-graph Construction
How to represent control flow in e-graph?
terminators
side-effects
control-flow
for
while
if
regions
blocks
control-flow ops
regions
roots
yield
store
condition
order matters!
pure computation pattern trees
+
-
-
<<
&
^
!
algebraic
rewrites
work!
cf
region
Tuple
terminators
side-effects
cf
pure
pure
root-based construction

## Slide 105: Hands-on Construction
Click
Application in MLIR
Initial E-Graph
statistics
Scroll down to view the complete matching process.
Part 1: E-graph Construction

## Slide 106: APS Compiler Workflow
Custom Instr(CADL)
Hybrid Rewrite Engine
Skeleton-components matching
Semantic Translation
Binary
Lowering passes
Existing tools
Key techniques
Initial
e-graph
Application (c-code)
Polygeist
Application
MLIR
E-graph
Construction
dataflow
Rewrite rules
MLIR
passes
ISAX
MLIR

## Slide 107: Hybrid Rewrite(I)
Internal rewrites: dataflow transformations
?a << 2  ?a x 4
Rules:
for
store
x
<<
i
4
2
1
step
for
store
<<
i
2
1
step

## Slide 108: Hybrid Rewrite(II)
Internal rewrite statistics in web demo
Scroll down to part 2.1

## Slide 109: Hybrid Rewrite(III)
External rewrites: control flow transformations
  MLIR passes and factors are guided by the control flow difference between Application and ISAX
for
store
x
<<
i
4
2
1
step
omit loop bounds
for (0, 4, 1):
A[i] = i * 4;
omit load…
for (0, 4, 2):
A[i] = i * 4;
A[i+1] = (i+1) * 4;
loop unroll 2
extract
for
store
store
step
union

## Slide 110: Hybrid Rewrite(IV)
External rewrite statistics in web demo
Scroll down to part 2.2
Guidance:
loop unroll
factor = 2

## Slide 111: Hybrid Rewrite(V)
...
scf.for %arg2 = %c0 to %c2 step %c1 {
%3 = scf.for %arg3 = %c0 to %c4 step %c1 iter_args(%arg4 = %c0) -> (i32) {
...
scf.yield %18 : i32
}
memref.store %3, %arg1[%4] : memref<?xi32>
%7 = scf.for %arg5 = %c0 to %c4 step %c1 iter_args(%arg6 = %0) -> (i32) {
...
scf.yield %19 : i32
}
memref.store %7, %arg1[%5] : memref<?xi32>
}
...
module {
func.func @vgemv3d_vv(%arg0: memref<?xi32>, %arg1: memref<?xi32>) -> i8 {
...
scf.for %arg2 = %c0 to %c4 step %c1 {
%3 = scf.for %arg3 = %c0 to %c4 step %c1 iter_args(%arg4 = %c0) -> (i32) {
...
scf.yield %18 : i32
}
memref.store %3, %arg1[%4] : memref<?xi32>
}
return %c0 : i8
}
}
Extracted one
After Loop pass
loop unroll
factor = 2
(0,4)
(0,2)

## Slide 112: Hybrid Rewrite(VI)
After the external rewrite, a new e-node “for” is merged to the origin e-class
click

## Slide 113: APS Compiler Workflow
Custom Instr(CADL)
Hybrid Rewrite Engine
Skeleton-components matching
Semantic Translation
Binary
Lowering passes
Existing tools
Key techniques
Initial
e-graph
Application (c-code)
Polygeist
Application
MLIR
E-graph
Construction
dataflow
Rewrite rules
MLIR
passes
ISAX
MLIR

## Slide 114: Skeleton-components Matching
For example, the pseudo instruction can be decomposed of a skeleton and 2 component rewrites
for i=0 to 4:
for j=0 to 4:
acc+=a[i<<2+j] * b
yield acc
store acc
yield (acc + a[i<<2+j] * b)
for(0, 4)
for(0, 4)
component 1
component 2
component 1
store acc
component 2


Skeleton:
cf + roots
Components:
Pattern trees

## Slide 115: Skeleton-components Matching
Details
  Decompose the ISAX into skeleton and component rewrites
…
Scroll down to part 3
egglog
rewrites

## Slide 116: Skeleton-components Matching
Details
  rewrite the application e-graph with component rewrites(in egglog)
# of e-classes/e-nodes

## Slide 117: Skeleton-components Matching
module {
func.func @vgemv3d_vv(%arg0: !llvm.ptr, %arg1: !llvm.ptr) -> i8 {
...
%2 = llvm.inline_asm has_side_effects ".insn r 0x2B, 0x7, 0x31, $0, $1, $2", "=r,r,r,~{memory}" %0, %1 : (i32, i32) -> i1
...
}
}
Details
  customized search the e-graph with skeleton
  validate dependencies and ordering. After that, add an e-node(ISAX)
  extract the e-graph and reconstruct the MLIR
Use llvm.inline_asm to call ISAX

## Slide 118: Result
Inserted instruction

## Slide 119: Other cases
  Your own cases: cd ~/aps && pixi run compile *.cadl *.c *.riscv
Click
Another cases

## Slide 120: Architecture and Deployment
Speaker: Yuyang Zou
邹羽洋

## Slide 121: Environment Setup
Before we start, please make sure you have entered our pixi environment by typing
  This will automatically configure the correct environment required to run APS toolchain.
  CHECK:
cd ~/aps && pixi shell
(aps-mlir) root@server:~/aps

## Slide 122: Outline
Processor Integration
  APS-Itfc (cont.)
  DMA Engine
Example (1): 3D-Point Cloud Analytics (VLSI Flow)
FPGA Deployment
Example (2): CPU LLM Inference (FPGA Flow)

## Slide 123: Recall: APS-Itfc
APS-Itfc, a unified interface for ISAXs’ seamless integration into different RISC-V platforms.
ISAX
datapath
controller
IF
IF/ID
ID/Ex
Ex/Mem
Mem/ Wb
LSU
RegFile
ISAX
decode & issue
RISC-V Platform
ISAX
APS-Itfc
…
PULP
Chipyard

## Slide 124: Recall: APS-Itfc
APS-Itfc models how ISAX interacts with the processor
RISC-V Platform
ISAX
APS-Itfc
Issue
Req
start a new execution
GPR
Req
receive operands
Rd/WrMem
Req
initiate
single mem read/write
Rd/WrMem
Resp
receive
single mem read/write result
Result
Resp
send back result
Rd/WrBlkMem
Req
initiate mem block
read/write
Rd/WrBlkMem Resp
receive mem block
read/write result

## Slide 125: Mapping APS-Itfc to Real Cores
Each ecosystem provides it’s own ISAX interfaces
Example: Chipyard’s RoCC
  Rocket Custom Coprocessor
  R-type instruction execution + L1D$ access
IF
IF/ID
ID/Ex
Ex/Mem
Mem/ Wb
LSU
RegFile
L1 D$
Rocket
RV32IMAC
RoCC
Design
rocc.cmd
rocc.resp
rocc.mem.resp
rocc.mem.req
// LazyRoCC.scala
class RoCCCoreIO {
val mem = new HellaCacheIO
val cmd = Flipped(Decoupled(new RoCCCommand))
val resp = Decoupled(new RoCCResponse)
// busy, intr, exception, csrs
}

## Slide 126: Implement APS-Itfc With RoCC
APS-Itfc is implemented as an adaptor circuit for each target
ISAX + Memory Pool
Rocket-core / BOOM
Rocket Custom Coprocessor (RoCC) interface
r/w
Buf
Slot 1
Buf
Slot 2
Reorder control
Issue Req
GPR Req
WrMem Req
RdMem Req
RdMem Resp
Result Resp
rocc.cmd
rocc.resp
rocc.mem
.resp
Other ISAXs omitted
dispatch
r/w
sel
sel
sel
sel
Buf Slot
tag
addr
data
RoCC Adaptor
WrBlkMem
Req
RdBlkMem
WrBlkMem
Resp
RdBlkMem
rocc.mem
.req

## Slide 127: Beyond RoCC…
RoCC’s single-element memory access is slow
  Performance bottleneck of vector/matrix ops in emerging domains
req
resp
2
3
4
2
4
3
6
5
Bubble
L=2
1
Re-order
Low bandwidth!
ISAX
System Bus
Processor
RoCC
Adaptor
rocc.mem
Cache
Mem
Pool
1

## Slide 128: Integrated DMA Engine
Accelerate batch data transfer via burst DMA transfer
Fast for vector/matrix data!
ISAX
System Bus
Processor
RoCC
Adaptor
rocc.mem
Cache
Mem
Pool
DMA
Engine

## Slide 129: DMA Engine: CPU Memory Access
DMA engine is a master agent located at the FrontBus of Rocket SoC
SystemBus
RocketTile
Rocket
PTW
L1D$
ISAX
DMA
Engine
FrontBus
L2$
MemoryBus
ControlBus
PeripheryBus
L1I$

## Slide 130: TileLink Protocol Basics
A free and open standard for tightly coupled, low-latency SoC buses, designed for RISC-V
  System bus protocol of Rocket SoC
  We use TL-UH, a subset of TileLink with burst transfer capability
TileLink Spec: https://www.sifive.com/document-file/tilelink-spec-1.9.3
Channel A
Channel D
Request messages sent to an address.
Response messages from an address.
2
Master
Interface
1
3
Slave
Interface
2
Slave
Interface
1

## Slide 131: DMA Engine: CPU Memory Access
Timing Characteristics
  Load data arrives after 15 cycles;
  A new data word is transferred per cycle.
  Store complete 5 cycles after the last data;
  One burst loads/store operate over a maximum of a D$ line-sized block into/from the ISAX.
Ch. A
Ch. D
2
3
4
N
…
L=15
R
1
Load (CPU Mem to ISAX Mem)
Ch. A
Ch. D
2
N
…
L=5
1
Store (ISAX Mem to CPU Mem)
Ack
Ack
…
Ack

## Slide 132: DMA Engine: CPU Memory Access
Accelerate memory load with dual channel DMA
Ch. A
Ch. D
A2
A3
A4
AN
…
L=2*(N+15)
AR
A1
Single Channel
BR
B2
B3
B4
BN
…
B1
Ch. A
Ch. D
A2
A3
A4
AN
…
L=2*N+15
AR
A1
Dual Channel
BR
B2
B3
B4
BN
…
B1
Preparation period overlapped!

## Slide 133: DMA: ISAX Memory Access
DMA employs address space mapping to access ISAX’s memory
  Address space is assigned during synthesis optimization stage
  A bus-width of data can be written to multiple banks according to the partition policy specified by directives
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
0x0
0x4
0x8
0xC
mat
Bank 0..3
i8
i8
i8
i8
0x10
vec
i8
i8
i8
i8
0x14
res
Bank 0..4
Bank 0..4
DMA Access
ISAX
RoCC
Adaptor
Mem
Pool
DMA
Engine
// tutorial-opt.mlir
module {
aps.memorymap {
aps.mem_entry ”mat" : banks([@mat]), base(0), size(16), count(1), cyclic(1)
aps.mem_entry ”vec" : banks([@vec]), base(16), size(4), count(1), cyclic(1)
aps.mem_entry ”res" : banks([@res]), base(20), size(4), count(1), cyclic(1)
aps.mem_finish
}
}

## Slide 134: DMA: ISAX Memory Access
DMA employs address space mapping to access ISAX’s memory
  Address space is assigned during synthesis optimization stage
  A bus-width of data can be written to multiple banks according to the partition policy specified by directives
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
0x0
0x4
0x8
0xC
mat
Bank 0..3
i8
i8
i8
i8
0x10
vec
i8
i8
i8
i8
0x14
res
Bank 0..4
Bank 0..4
DMA Access
ISAX
RoCC
Adaptor
Mem
Pool
DMA
Engine
A: 0xC
D: 0xdeadbeef
0xef
0xbe
0xad
0xde

## Slide 135: DMA: ISAX Memory Access
DMA engine can also directly apply layout transformations, eliminating on-core rearrangement overhead.
  Example: Tiling
// tiling.cadl
[[stride_x(2)]]
[[stride_y(2)]]
mat[sa +: ] = _burst_read[da +: 8];
DRAM
ISAX
(Cyclic-Parted)
(Factor=2)
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8

## Slide 136: DMA: ISAX Memory Access
DMA engine can also directly apply layout transformations, eliminating on-core rearrangement overhead.
  Example: Tiling
// tiling.cadl
[[stride_x(2)]]
[[stride_y(2)]]
mat[sa +: ] = _burst_read[da +: 8];
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
DRAM
ISAX
(Cyclic-Parted)
(Factor=2)
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8

## Slide 137: DMA: ISAX Memory Access
DMA engine can also directly apply layout transformations, eliminating on-core rearrangement overhead.
  Example: Tiling
// tiling.cadl
[[stride_x(2)]]
[[stride_y(2)]]
mat[sa +: ] = _burst_read[da +: 8];
DRAM
ISAX
(Cyclic-Parted)
(Factor=2)
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8

## Slide 138: DMA: ISAX Memory Access
DMA engine can also directly apply layout transformations, eliminating on-core rearrangement overhead.
  Example: Tiling
// tiling.cadl
[[stride_x(2)]]
[[stride_y(2)]]
mat[sa +: ] = _burst_read[da +: 8];
DRAM
ISAX
(Cyclic-Parted)
(Factor=2)
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8
i8

## Slide 139: APS-Itfc Adaptor
We are ready to elaborate the whole processor!
ISAX + Memory Pool
Rocket-core / BOOM
Rocket Custom Coprocessor (RoCC) interface
r/w
Buf
Slot 1
Buf
Slot 2
Reorder control
Issue Req
GPR Req
WrMem Req
RdMem Req
RdMem Resp
Result Resp
RoCC Req
RoCC Resp
Hella Req
Hella Resp
Other ISAXs omitted
dispatch
r/w
sel
sel
sel
sel
Buf Slot
tag
addr
data
RoCC Adaptor
TileLink Interface
DMA Engine
Layout Transform
Multi-channel
CH.A
Burst-capable
CH.D
WrBlkMem
Req
RdBlkMem
WrBlkMem
Resp
RdBlkMem
Find verilog files at:
${APS_CHIPYARD}/ generators/aps/src/main/resources/vsrc

## Slide 140: Example (1): 3D-Point Cloud Analytics
Point cloud analysis is an essential computational workload in spatial machine vision technologies
  Two critical algorithm: FPS and KNN
FPS (Farthest Point Sampling)
Iteratively select the point with max distance to the sample set
kNN (k-Nearest Neighbor Search)
FPS Image Source: Dehghanpour, A., Sharifi, Z. & Dehyadegari, M. Point cloud downsampling based on the transformer features. Vis Comput 41, 2629–2638 (2025).
k=3
k=7
Identify
Select number of point with the min distance to the query point

## Slide 141: Example (1): 3D-Point Cloud Analytics
Task: Compute the squared Euclidean distance between corresponding points in two point clouds (16 points each)
Solution: Custom Instruction “v3ddist.vv”
  Parameters:
    rs1: Memory address of two point clouds (contiguously, SOA layout, uint32);
    rs2: Output distance array (uint32);
    rd: Return value, fixed at 0
  Encoding:
    R-type, opcode=7‘b0101011, funct7=7'b0101000, funct3=3’b111 (RoCC)
x0
x1
x2
x3
x4
y0
y1
y2
y3
y4
z0
z0
z1
z2
z3
SOA layout: Axis First, Element Last

## Slide 142: Example (1): 3D-Point Cloud Analytics
CADL Description:
// v3ddist_vv_basic.cadl
static points1_x: [u32; 16];
static points1_y: [u32; 16];
static points1_z: [u32; 16];
static points2_x: [u32; 16];
static points2_y: [u32; 16];
static points2_z: [u32; 16];
static dist_out: [u32; 16];
#[opcode(7'b0001011)]
#[funct7(7'b0101000)]
rtype v3ddist_vv(rs1: u5, rs2: u5, rd: u5) {
let addr1: u32 = _irf[rs1];
let out_addr: u32 = _irf[rs2];
points1_x[0 +: ] = _burst_read[addr1 +: 16];
points1_y[0 +: ] = _burst_read[addr1 + 64 +: 16];
points1_z[0 +: ] = _burst_read[addr1 + 128 +: 16];
points2_x[0 +: ] = _burst_read[addr1 + 192 +: 16];
points2_y[0 +: ] = _burst_read[addr1 + 256 +: 16];
points2_z[0 +: ] = _burst_read[addr1 + 320 +: 16];
with i: u32 = (0, i + 1) do {
let dx: u32 = points1_x[i] - points2_x[i];
let dy: u32 = points1_y[i] - points2_y[i];
let dz: u32 = points1_z[i] - points2_z[i];
dist_out[i] = dx * dx + dy * dy + dz * dz;
} while (i + 1 < 16);
_burst_write[out_addr +: 16] = dist_out[0 +: ];
_irf[rd] = 0;
}
Find this file at:
${APS}/tutorial/cadl/v3ddist_vv_basic.cadl

## Slide 143: Example (1): 3D-Point Cloud Analytics
CADL Description:
#[opcode(7'b0001011)]
#[funct7(7'b0101000)]
rtype v3ddist_vv(rs1: u5, rs2: u5, rd: u5) {
let addr1: u32 = _irf[rs1];
let out_addr: u32 = _irf[rs2];
points1_x[0 +: ] = _burst_read[addr1 +: 16];
points1_y[0 +: ] = _burst_read[addr1 + 64 +: 16];
points1_z[0 +: ] = _burst_read[addr1 + 128 +: 16];
points2_x[0 +: ] = _burst_read[addr1 + 192 +: 16];
points2_y[0 +: ] = _burst_read[addr1 + 256 +: 16];
points2_z[0 +: ] = _burst_read[addr1 + 320 +: 16];
with i: u32 = (0, i + 1) do {
let dx: u32 = points1_x[i] - points2_x[i];
let dy: u32 = points1_y[i] - points2_y[i];
let dz: u32 = points1_z[i] - points2_z[i];
dist_out[i] = dx * dx + dy * dy + dz * dz;
} while (i + 1 < 16);
_burst_write[out_addr +: 16] = dist_out[0 +: ];
_irf[rd] = 0;
}
Read two address from regfile
Load point cloud data from DRAM to ISAX memory using DMA engine
Calculate pair-wise distance square
Burst store back to DRAM
Write zero to regfile

## Slide 144: Example (1): 3D-Point Cloud Analytics
Run faster?
  Apply Optimizations
  Example: Loop unroll
#[opcode(7'b0001011)]
#[funct7(7'b0101000)]
rtype v3ddist_vv(rs1: u5, rs2: u5, rd: u5) {
let addr1: u32 = _irf[rs1];
let out_addr: u32 = _irf[rs2];
points1_x[0 +: ] = _burst_read[addr1 +: 16];
points1_y[0 +: ] = _burst_read[addr1 + 64 +: 16];
points1_z[0 +: ] = _burst_read[addr1 + 128 +: 16];
points2_x[0 +: ] = _burst_read[addr1 + 192 +: 16];
points2_y[0 +: ] = _burst_read[addr1 + 256 +: 16];
points2_z[0 +: ] = _burst_read[addr1 + 320 +: 16];
with i: u32 = (0, i + 1) do {
let dx: u32 = points1_x[i] - points2_x[i];
let dy: u32 = points1_y[i] - points2_y[i];
let dz: u32 = points1_z[i] - points2_z[i];
dist_out[i] = dx * dx + dy * dy + dz * dz;
} while (i + 1 < 16);
_burst_write[out_addr +: 16] = dist_out[0 +: ];
_irf[rd] = 0;
}
We can unroll this loop by 4x!
[[unroll(4)]]
with i: u32 = (0, i + 1) do {
Find this file at:
${APS}/tutorial/cadl/ v3ddist_vv.cadl

## Slide 145: Example (1): 3D-Point Cloud Analytics
Run faster?
  Apply Optimizations
// v3ddist_vv.cadl
#[partition_dim_array([0])]
#[partition_factor_array([4])]
#[partition_cyclic_array([1])]
static ARRAYNAME: [u32; 16];
Apply partition on the first dimention
Apply cyclic partition with factor 4
16 elements in array, each 32bit unsigned
Loop unroll should be used together with array partition to fully utilize the parallism
Find this file at:
${APS}/tutorial/cadl/v3ddist_vv.cadl
#[partition_dim_array([0])]
#[partition_factor_array([4])]
#[partition_cyclic_array([1])]
static points1_x: [u32; 16];
// ... omitted...
static points1_y: [u32; 16];
// ... omitted...
static points1_z: [u32; 16];
// ... also for points2_*
#[partition_dim_array([0])]
#[partition_factor_array([4])]
#[partition_cyclic_array([1])]
static dist_out: [u32; 16];

## Slide 146: Synthesis the ISAX to RTL
Synthesis (1/3)
  (1) Run CADL-to-MLIR parser:
  It should look like this:
cd $APS/tutorial && pixi run mlir cadl/v3ddist_vv.cadl outputs/v3ddist_vv.mlir
CADL Parser
Input CADL File
Output Pre-opt MLIR File
module {
memref.global @points1_x : memref<16xi32> {...}
func.func @flow_v3ddist_vv(%arg0: i5, %arg1: i5, %arg2: i5)
attributes {funct7 = 40 : i32, opcode = 43 : i32} {
%0 = aps.readrf %arg0 : i5 -> i32
%1 = aps.readrf %arg1 : i5 -> i32
%2 = memref.get_global @points1_x : memref<16xi32>
%c0_i32 = arith.constant 0 : i32
%c16_i32 = arith.constant 16 : i32
// ...
}
}
cat outputs/v3ddist_vv.mlir
OR RUN: cd $APS/tutorial && bash a1-ex1synth.sh

## Slide 147: Synthesis the ISAX to RTL
Synthesis (2/3)
  (2) Run APS Synthesis tool to generate Cement HDL design:
  It should look like this:
pixi run opt outputs/v3ddist_vv.mlir outputs/v3ddist_vv_cmt.mlir
APS-Synthesis
Input MLIR File
Output Cement MLIR File
module {
cmt2.circuit {
cmt2.interface @BurstDMAController {
cmt2.method @cpu_to_isax_ch0 (...) -> () {
cmt2.return
} {
cmt2.return
}
}
// ...
}
}
cat outputs/v3ddist_vv_cmt.mlir
OR RUN: cd $APS/tutorial && bash a1-ex1synth.sh

## Slide 148: Synthesis the ISAX to RTL
Synthesis (3/3)
  (3) Run Cement’s RTL elaborate tool to produce SystemVerilog file
  It should look like this:
pixi run sv outputs/v3ddist_vv_cmt.mlir outputs/v3ddist_vv.sv
Cement Tool
Input Cement HDL File
Output SystemVerilog RTL File
// Generated by CIRCT 1f696a2b7
// Include register initializers in init blocks unless synthesis is set
`ifndef RANDOMIZE
`ifdef RANDOMIZE_REG_INIT
`define RANDOMIZE
`endif // RANDOMIZE_REG_INIT
`endif // not def RANDOMIZE
`ifndef SYNTHESIS
// ...
cat outputs/v3ddist_vv.sv
This step will take ~1minute!!!
OR RUN: cd $APS/tutorial && bash a1-ex1synth.sh

## Slide 149: Compile Target Workloads
Compile
  Run APS compiler (megg) to compile the workload with our customized ISAX
pixi run compile cadl/v3ddist_vv.cadl csrc/test_v3ddist_vv.c outputs/v3ddist_vv.riscv
APS-Compiler
Input CADL File
Output RISC-V Binary
=== Compilation Complete ===
Executable: v3ddist_vv.riscv
Intermediate files: compile_logs/
Generated files:
total 988
-rw-rw-r-- 1 user user 770759 Jan 11 20:49 v3ddist_vv.asm
-rw-rw-r-- 1 user user 1190 Jan 11 20:48 v3ddist_vv.c
-rw-rw-r-- 1 user user 68 Jan 11 20:48 v3ddist_vv.json
-rw-rw-r-- 1 user user 1417 Jan 11 20:48 v3ddist_vv.mlir
-rwxrwxr-x 1 user user 210520 Jan 11 20:49 v3ddist_vv.riscv
-rw-rw-r-- 1 user user 278 Jan 11 20:49 v3ddist_vv.stats.json
Input C Program File
OR RUN: cd $APS/tutorial && bash a2-ex1compile.sh

## Slide 150: Compile Target Workloads
Compile
  Check assembly file to check if ISAX is correctly applied, run:
cat outputs/compile_logs/v3ddist_vv.asm | grep -v f1202573 | grep insn -C 5
101a0: 00000317 auipc t1,0x0
101a4: 00000067 jr zero # 0 <exit-0x100b4>
101a8: 00008067 ret
000101ac <v3ddist_vv>:
101ac: 50b5752b .insn 4, 0x50b5752b
101b0: 00000513 li a0,0
101b4: 00008067 ret
000101b8 <get_march>:
101b8: fff50513 addi a0,a0,-1
OR RUN: cd $APS/tutorial && bash a3-ex1objdump.sh
Our ISAX
Filter out fake target
Here it is!

## Slide 151: Compile Target Workloads (Baseline)
Compile
  Also compile a baseline version without ISAX, run
  Check there’s no ISAX calling in baseline binary, run
    We expect NO outputs from terminal
OR RUN: cd $APS/tutorial && bash a4-ex1native.sh
pixi run compile-native csrc/test_v3ddist_vv.c outputs/v3ddist_vv_native.riscv
RISC-V Native Compiler
Input C Program File
Output RISC-V Binary
pixi run riscv32-unknown-elf-objdump -j .text –D outputs/v3ddist_vv_native.riscv | grep -v f1202573 | grep insn -C 5

## Slide 152: Processor Integration: Chipyard
We use a JSON file (aps_config.json) to integrate Chipyard to our workflow
  It looks like this:
// aps_config.json
{
"backend": "rocc",
"arch": "rv32",
"core_count": 1,
"top_module": "aps_rocc_wrapper",
"name": "aps_rocc_module",
"vsrc": [
"wrapper_dma_trig.sv",
"tl_dma_2ch_v2.sv",
"v3ddist_vv.sv"
],
"maxBurstBytes": 128,
"nXacts": 2
}
Please modify this file only when using different ISAX path
Find this file at:
${APS_CHIPYARD}/ aps_config.json
rv32/rv64
Number of Rocket core
ISAX source file (Change here if required)
Number of DMA Channels
Maximum transfer bytes each burst

## Slide 153: RTL Simulation
Use Chipyard to elaborate the whole processor, and simulate it with Verilator
  First run without ISAX
  Then run with ISAX
cd $APS_CHIPYARD/sims/verilator &&
make CONFIG=APSRocketConfig run-binary-debug BINARY=$APS/tutorial/outputs/v3ddist_vv.riscv LOADMEM=1 -j4
cd $APS_CHIPYARD/sims/verilator &&
make CONFIG=APSRocketConfig run-binary-debug BINARY=$APS/tutorial/outputs/v3ddist_vv_native.riscv LOADMEM=1 -j4
OR RUN: cd $APS/tutorial && bash a5-ex1nativesim.sh
OR RUN: cd $APS/tutorial && bash a6-ex1sim.sh

## Slide 154: Performance
Each output will show the result and performance
Used 166 cycles
Computed results:
[ 1]: (10,5,100) <-> (15,10,110)=150
[ 2]: (20,15,200) <-> (25,20,210)=150
[ 3]: (30,25,300) <-> (35,30,310)=150
[ 4]: (40,35,400) <-> (45,40,410)=150
// ...omitted
[16]: (160,155,1600)<->(165,160,1610)=150
Without ISAX
(v3ddist_vv_native.riscv)
With ISAX
(v3ddist_vv.riscv)
4.14x performance improvement
Used 688 cycles
Computed results:
[ 1]: (10,5,100) <-> (15,10,110)=150
[ 2]: (20,15,200) <-> (25,20,210)=150
[ 3]: (30,25,300) <-> (35,30,310)=150
[ 4]: (40,35,400) <-> (45,40,410)=150
// ...omitted
[16]: (160,155,1600)<->(165,160,1610)=150

## Slide 155: VLSI Flow
We use yosys + OpenROAD for logic synthesis and PnR
  Scripts are located at $APS_CHIPYARD/nextvlsi
  Open-source PDK and stdcell: IHP130 and sg13g2
  Run logic synthesis:
  Synthesis takes ~10 minutes to finish
  PnR is slower, we don’t run it here
cd $APS_VLSI && make yosys CONFIG=APSRocketConfig
OR RUN: cd $APS_VLSI && bash a7-ex1yosys.sh

## Slide 156: Logic Synthesis Result
Synthesis report will be available at
To simplify the result, run
You will get
$APS_CHIPYARD/nextvlsi/yosys/default/reports/RocketTile_area.rpt
cd $APS/tutorial/ && python vlsi-report-simplify.py
Synthesis report
=============================
Original processor’s area: 4230122.10 um²
Your design’s area: 1351298.67 um² (+31.94% overhead)
=============================
$APS_CHIPYARD/nextvlsi/yosys/default/reports/RocketTile_area_rocc.rpt

## Slide 157: FPGA Deployment
FPGA deployment flow on AMD ZYNQ platform, including
  Vivado block-design workflow for PL logic (RISC-V)
  Pre-built Petalinux image for PS core (ARM)
  Programming and monitoring tool (APS-prog, built upon fesvr)
RJ45
UART
AMD Xilinx
ZC706
(XC7Z045)
SD
BOOT.BIN
Linux kernel
Linux rootfs
…
UART
ETH
…
PL DDR
PS Core
(ARM)
PS UART
PS ETH
PS SDIO
AXI
GP0
PL Core
(APS)
fbus
fbus
pbus
+ APS-Prog

## Slide 158: FPGA Deployment
Vivado block design for ZC706 development board
  AMD ZYNQ 7045, 218k LUTs, 437k FFs, 19.2Mb BRAM, 900 DSPs
  Runs rocket-core (Small, 1 Core) at ~80MHz

## Slide 159: FPGA Deployment
APS-Prog: Programming and monitoring tool
  Program RISC-V core using UIO via PS-PL AXI interface
  Runs on Petalinux inside PS ARM core
  Example:
aps_petalinux:~$ ./aps_prog
MMIO-based HTIF for FPGA Rocket Core
Usage: ./aps_prog +uio=/dev/uioX [OPTIONS] <binary>
sudo ./aps_prog +uio=/dev/uio0 ~/hello.riscv

## Slide 160: Example (2): CPU LLM Inference
LLM inference is fundamentally GEMV-bound
  We profiled llama2.c on target RISC-V platform
  GEMV contributes to 90% latency
Profiling:
==========================
%time calls name
--------------------------
89.55 5332 gemv
2.99 248 sample_topp
1.49 124 forward
void kernel_gemv(int ni, int nj,
DATA_TYPE A[NI][NJ],
DATA_TYPE x[NJ],
DATA_TYPE y[NI]) {
int i, j;
for (i = 0; i < ni; i++) {
DATA_TYPE tmp = 0.0;
for (j = 0; j < nj; j++) {
tmp += A[i][j] * x[j];
}
y[i] = y[i] + tmp;
}
}

## Slide 161: Example (2): CPU LLM Inference
GEMV kernels in LLM inference are huge
  Placing the whole matrix or vector in SRAM is unpractical
  AMD ZYNQ 7045: 19.2Mb BRAM
  Apply tiling is a must
Animation modified based on: https://towardsdatascience.com/hey-gpu-whats-up-with-my-matrix-cb7f6d7ae7d6/
Operations | GEMV Size
Attention Projection | [1x288] x [288x288]
FFN | [1x288] x [288x768]
 | [1x768] x [768x288]
Vocabulary | [1x288] x [288x32000]
A Tile

## Slide 162: Example (2): CPU LLM Inference
Tiling strategy
  Tile Size: 8x16
Quantization
  W8A8
  int32 accumulation
Scratchpad memory
  matA: int8, 256KB
  vecB: int8, 128KB
  vecC: int32, 256KB
// inference.cadl
#[partition_dim_array([0])]
#[partition_factor_array([16])]
#[partition_cyclic_array([1])]
static matA: [i8; 262144]; // 256KB
#[partition_dim_array([0])]
#[partition_factor_array([16])]
#[partition_cyclic_array([1])]
static vecB: [i8; 131072]; // 128KB
#[partition_dim_array([0])]
#[partition_factor_array([8])]
#[partition_cyclic_array([1])]
static vecC: [i32; 65536]; // 256KB
Find this file at: $APS/tutorial/cadl/inference.cadl

## Slide 163: Example (2): CPU LLM Inference
Moving from and to ISAX memory: matA
  Load mat
// inference.cadl
#[opcode(7'b1111011)]
#[funct7(7'b0000000)]
rtype loadmat_a_4tile(rs1: u5,rs2: u5,rd: u5) {
let dram_addr0: u32 = _irf[rs1];
let r2: u32 = _irf[rs2];
let spm_addr0: u32 = r2 >> 16;
let block_w: u32 = (r2 & 32'hFFFF);
[[unroll(8)]]
with
i: u32 = (0, i_)
dram_addr: u32 = (dram_addr0, dram_addr_)
spm_addr : u32 = (spm_addr0, spm_addr_)
do {
} while (i_ < 8);
_irf[rd] = 0;
}
[[stride_x(16)]]
[[stride_y(8)]]
matA[spm_addr +: ] =
_burst_read[dram_addr +: 64];
let dram_addr_: u32 = dram_addr + block_w;
let spm_addr_: u32 = spm_addr + 16;
let i_: u32 = i + 1;
...
...
N_TILES = N / 16
M_TILES = M / 8
Load 4 consequtive tiles each call
block_w = N * sizeof(int8) = N
Find this file at:
$APS/tutorial/cadl/inference.cadl
rs1: DRAM address
rs2[31:16]: ISAX Memory address
rs2[15:0]: Matrix width (block_w)
A Tile
(8x16, int8)

## Slide 164: Example (2): CPU LLM Inference
Moving from and to ISAX memory: vecB and vecC
  Also provide load 32B/256B vector B and store 128B/256B vector C
  rs1: DRAM address, r2[31:15]: ISAX memory address
Find this file at: $APS/tutorial/cadl/inference.cadl

## Slide 165: Example (2): CPU LLM Inference
Compute GEMV
  Instruction Behavior:
  Instruction format: Opcode=7'b0001011, Funct7=7’b0000000
[31:16] | 15 | [14:0]
31
0
16
15
rs1
offsetA: Start address of matA memory
14
 | [15:0]
0
15
offsetB: Start address of vecB memory
offsetC: Start address of vecC memory
rs2
useC: 1: Do accumulation on C[i]; 0: Overwrite

## Slide 166: Example (2): CPU LLM Inference
Compute GEMV
// inference.cadl
#[opcode(7'b0001011)]
#[funct7(7'b0000000)]
rtype gemv16_i8(rs1: u5,rs2: u5,rd: u5)
{
let r1: u32 = _irf[rs1];
let r2: u32 = _irf[rs2];
let offsetA: u16 = r1 >> 16;
let offsetB: u16 = r1 & 32'h7FFF;
let offsetC: u16 = r2 & 32'hFFFF;
let use_c: u1 = (r1 >> 15) & 1;
with i: u32 = (0, i_) do {
} while (i_ < 8);
_irf[rd] = 0;
}
zacc = 0;
[[unroll(16)]]
with k: u32 = (0, k_) do {
let a_idx: u32 = i*16 +k +offsetA*128;
let a_val: i32 = matA[a_idx];
let b_idx: u32 = k + offsetB * 16;
let b_val: i32 = matB[b_idx];
zacc = zacc + a_val * b_val;
let k_: u32 = k + 1;
} while (k_ < 16);
let c_idx: u32 = i + offsetC * 8;
let c_val_raw: i32 = matC[c_idx];
let c_val: i32 = if (use_c) {c_val_raw}
else {32'h0};
let c_out: i32 = zacc + c_val;
matC[c_idx] = c_out;
let i_: u32 = i + 1;
Find this file at: $APS/tutorial/cadl/inference.cadl

## Slide 167: Synthesis and Compiling
Run synthesis
Run compiler
  It will produce inference.riscv (with ISAX) and inference_native.riscv (without ISAX) in outputs/
OR RUN: cd $APS/tutorial && bash a8-ex2synth.sh
pixi run sv outputs/inference_cmt.mlir outputs/inference.sv
pixi run opt outputs/inference.mlir outputs/inference_cmt.mlir
cd $APS/tutorial && pixi run mlir cadl/inference.cadl outputs/inference.mlir
We recommend to use this
cd $APS/tutorial && bash a9-ex2compile.sh

## Slide 168: FPGA Deployment
FPGA Prototyping
  Try it out after this tutorial if you have ZC706 board and basic knowledge of ZYNQ development!
  (1) Replace “ISAX.sv” in APS-FPGA Project with “inference.sv”;
  (2) Run Vivado Synthesis, PnR, and generate bitstream;
  (3) Use “petalinux-package” to generate BOOT.BIN;
  (4) Format your SD card into two partition, format the first partition in FAT32;
  (5) copy BOOT.BIN, boot.scr, and image.ub to the first partition;
  (6) Use “dd” to copy our rootfs to the second partition.

## Slide 169: Performance
FPGA Prototyping
  Load the binary “inference.riscv” and “inference_native.riscv”
  Run: sudo ./aps_prog ~/inference.riscv OR ~/inference_native.riscv
  Baseline (~0.24tok/s)
  APS (~1.19tok/s)